## Slide 1: Computer Architecture Lecture 22c: MQSim
Rakesh Nadig
Prof. Onur Mutlu
ETH Zürich
Fall 2023
8 December 2023

## Slide 2: Introduction
Rakesh Nadig
  PhD Student @ SAFARI research group since 2021
  Previously worked at Samsung Electronics
  MS in Electrical and Computer Engineering from University of California Irvine
Research Interests
  Memory/Storage Systems
  NAND Flash Memory
  Near-Storage Processing
  Machine Learning
  Hybrid Memory/Storage Systems
Contact
  rakesh.nadig@safari.ethz.ch
  https://www.linkedin.com/in/rakeshnadig/
  https://twitter.com/rakeshnadig2404

## Slide 3: MQSim A Framework for Enabling Realistic Studies of Modern Multi-Queue SSD Devices
Arash Tavakkol, Juan Gómez-Luna, Mohammad Sadrosadati, Saugata Ghose, Onur Mutlu
FAST 2018

## Slide 4: Executive Summary
Solid-state drives (SSDs) are evolving to keep pace with performance, storage density demands
  Multi-queue SSDs (MQ-SSDs) use new host protocols (e.g., NVMe)
  New SSDs make use of emerging storage technologies (e.g., PCM, 3D XPoint)
Existing simulators have not kept up with these changes
  They do not support several major features: multi-queue protocols, efficient steady-state SSD models, full end-to-end request latency
  Compared to real MQ-SSDs, best existing simulator has 68–85% error rate
We introduce MQSim, a new open-source simulator
  Models all major features of conventional SSDs and newer MQ-SSDs
  Available with full-system simulator integration: accurate application modeling
  Enables several new research directions
MQSim is highly accurate
  Validated against four real MQ-SSDs
  Error rate for real workloads: 6–18%
http://github.com/CMU-SAFARI/ MQSim

## Slide 5: Outline
Executive Summary
Looking Inside a Modern SSD
Challenges of Modeling Modern Multi-Queue SSDs
MQSim: A New Simulator for Modern SSDs
Evaluating MQSim Accuracy
Research Directions Enabled by MQSim
Conclusion

## Slide 6: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)

## Slide 7: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host

## Slide 8: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host
  Flash Translation Layer (FTL): manages resources, processes I/O requests

## Slide 9: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host
  Flash Translation Layer (FTL): manages resources, processes I/O requests
  Flash Channel Controllers (FCCs): sends commands to, transfers data with memory chips in back end

## Slide 10: FTL: Managing the SSD’s Resources
Flash writes can take place only to pages that are erased
  Perform out-of-place updates (i.e., write data to a different, free page), mark old page as invalid
  Update logical-to-physical mapping (makes use of cached mapping table)
  Some time later: garbage collection reclaims invalid physical pages off the critical path of latency

## Slide 11: FTL: Managing the SSD’s Resources
Flash writes can take place only to pages that are erased
  Perform out-of-place updates (i.e., write data to a different, free page), mark old page as invalid
  Update logical-to-physical mapping (makes use of cached mapping table)
  Some time later: garbage collection reclaims invalid physical pages off the critical path of latency
Write cache: decreases resource contention, reduces latency

## Slide 12: Outline
Executive Summary
Looking Inside a Modern SSD
Challenges of Modeling Modern Multi-Queue SSDs
MQSim: A New Simulator for Modern SSDs
Evaluating MQSim Accuracy
Research Directions Enabled by MQSim
Conclusion

## Slide 13: How Well Do Simulators Model Modern SSDs?
State-of-the-art simulators designed for conventional SSDs
We compare the performance of several simulators to four real modern multi-queue SSDs (MQ-SSDs)
Major features missing in most existing simulators
  Multi-queue protocols (e.g., NVMe)
  Efficient, high-performance model of steady-state behavior
  Full model of end-to-end request latency
Simulator | Error Rate vs. Real MQ-SSDs |  |  | 
 | SSD-A | SSD-B | SSD-C | SSD-D
SSDModel | 91% | 155% | 196% | 136%
FlashSim | 99% | 259% | 310% | 138%
SSDSim | 70% | 68% | 74% | 85%
WiscSim | 95% | 277% | 324% | 135%
Why is the error rate so high?

## Slide 14: Challenge 1: Support for Multi-Queue Protocols
Conventional host interface (e.g., SATA)
  Designed for magnetic hard disk drives: only thousands of IOPS per device
  OS handles scheduling, fairness control for I/O requests
Process 1
Process 2
Process 3
OS Block Layer
SSD Device
Hardware dispatch queue
I/O Scheduler
Software
I/O Request
Queue

## Slide 15: Challenge 1: Support for Multi-Queue Protocols
Modern host interface (e.g., NVMe)
  Takes advantage of SSD throughput: enables millions of IOPS per device
  Bypasses OS intervention: SSD must perform scheduling, ensure fairness
Process 1
Process 2
Process 3
SSD Device
Hardware
I/O Request
Queue
No existing SSD simulator models this today
In the paper: studies on how multiple queues in real MQ-SSDs affect performance, fairness

## Slide 16: Challenge 2: High-Performance Steady-State Model
SNIA: SSDs should be evaluated in steady state
  Fresh, out-of-the-box (FOB) device unlikely to perform garbage collection
  Write cache not warmed up for an FOB device
Many previous SSD studies incorrectly simulate FOB devices
Difficult to reach steady state in most simulators
  Very slow (e.g., SSDSim execution time increases by up to 80x)
  Widely-used traces aren’t large enough for proper warm-up
Existing simulators either don’t model steady state or are slow at reaching steady state
Total Write
Volume (GB)
Workloads

## Slide 17: Challenge 3: Complete Model of Request Latency
Request to NAND flash based SSD
Current simulators often model only steps 5 and 6
What if we use a different non-volatile memory (NVM)?
< 1µs
50-110µs
20µs
4µs
50-110µs
20µs
< 1µs
< 1µs
< 1µs

## Slide 18: Challenge 3: Complete Model of Request Latency
Request to 3D XPoint based SSD
< 1µs
50-110µs
20µs
4µs
10-20µs
< 5µs
< 5µs
10-20µs
Existing simulators don’t model all parts of the request latency, causing inaccuracies for new NVMs
< 1µs
< 1µs
< 1µs

## Slide 19: Summary: Simulation Challenges of MQ-SSDs
Major features missing in most existing simulators
  Multi-queue protocols (e.g., NVMe)
  Efficient, high-performance model of steady-state behavior
  Full model of end-to-end request latency
Missing features lead to high inaccuracy
OUR GOAL
Develop a new simulator that faithfully models features of both modern MQ-SSDs and conventional SSDs

## Slide 20: Outline
Executive Summary
Looking Inside a Modern SSD
Challenges of Modeling Modern Multi-Queue SSDs
MQSim: A New Simulator for Modern SSDs
Evaluating MQSim Accuracy
Research Directions Enabled by MQSim
Conclusion

## Slide 21: Major Features of MQSim
Accurately models conventional SATA-based SSDs and modern MQ-SSDs
  Multi-queue protocols
  Support for efficient modeling of steady-state behavior
  Full model of end-to-end I/O request latency
Flexible design
  Modular components
  Ability to support emerging non-volatile memory (NVM) technologies
Open-source release: http://github.com/CMU-SAFARI/MQSim
  Written in C++
  MIT License
Notes: SATA: Native Command Queue

## Slide 22: Experimental Methodology
Compare MQSim to four real, modern data center SSDs
  System config: Intel Xeon E3-1240, 32GB DDR4, Ubuntu 16.04.2
  All SSDs use NVMe protocol over PCIe bus
  Real SSDs preconditioned by writing to 70% of available logical space
  MQSim parameters set to model each SSD
We test using multiple I/O flows (1 flow = 1 application)
  Queue depth controls flow greediness (number of simultaneous requests)
  We show representative results here; full results in our paper

## Slide 23: MQSim Multi-Queue Model
Inter-flow interference exists in many state-of-the-art SSDs
Real SSD
MQSim
Flow 1
Flow 2
Flow 2
Flow 1
Slowdown
Slowdown
Fairness
Flow 2 Queue Depth
Flow 2 Queue Depth
Flow 2 Queue Depth
Norm. Throughput
Norm. Throughput
Slowdown
Slowdown
Fairness
Flow 2 Queue Depth
Flow 2 Queue Depth
Flow 2 Queue Depth
Norm. Throughput
Norm. Throughput
MQSim accurately captures inter-flow interference when one of two flows hogs I/O request bandwidth

## Slide 24: MQSim Multi-Queue Model
Some SSDs have mechanisms to control inter-flow interference
Real SSD
MQSim
Slowdown
Slowdown
Fairness
Flow 2 Queue Depth
Flow 2 Queue Depth
Flow 2 Queue Depth
Norm. Throughput
Norm. Throughput
Slowdown
Slowdown
Fairness
Flow 2 Queue Depth
Flow 2 Queue Depth
Flow 2 Queue Depth
Norm. Throughput
Norm. Throughput
Flow 1
Flow 2
Flow 2
Flow 1
MQSim models the impact of control mechanisms for inter-flow interference in modern MQ-SSDs

## Slide 25: Capturing Steady-State Behavior with MQSim
MQSim includes an efficient SSD preconditioning mechanism
  Very fast: does not need to execute actual requests
  Can be disabled to simulate fresh, out-of-the-box (FOB) device
Two-pass approach
  Read input trace, perform statistical analysis
  Scan entire storage space, change status of each physical page based on analysis
Response time (RT) differences between FOB SSDs,
SSDs in steady state
With preconditioning, MQSim accurately captures the behavior of FOB SSDs and steady-state SSDs

## Slide 26: Outline
Executive Summary
Looking Inside a Modern SSD
Challenges of Modeling Modern Multi-Queue SSDs
MQSim: A New Simulator for Modern SSDs
Evaluating MQSim Accuracy
Research Directions Enabled by MQSim
Conclusion

## Slide 27: MQSim Accurately Captures Read/Write Latencies
Evaluations using two synthetic flows
Flow A: All Read Requests
Flow B: All Write Requests
Error rate vs. real SSDs, averaged across all four SSDs
Read latency: 2.9% Write latency: 4.9%

## Slide 28: MQSim Is More Accurate Than Existing Simulators
Experiments using three real workload traces
  Microsoft enterprise traces: TPC-C, TPC-E, Exchange Server
  Comparison of total workload execution time
  MQSim has a comparable execution time to other simulators
Simulator | Error Rate vs. Real MQ-SSDs |  |  | 
 | SSD-A | SSD-B | SSD-C | SSD-D
SSDModel | 91% | 155% | 196% | 136%
FlashSim | 99% | 259% | 310% | 138%
SSDSim | 70% | 68% | 74% | 85%
WiscSim | 95% | 277% | 324% | 135%
MQSim | 8% | 6% | 18% | 14%
MQSim is an order of magnitude more accurate at modeling MQ-SSDs than state-of-the-art simulators

## Slide 29: Outline
Executive Summary
Looking Inside a Modern SSD
Challenges of Modeling Modern Multi-Queue SSDs
MQSim: A New Simulator for Modern SSDs
Evaluating MQSim Accuracy
Research Directions Enabled by MQSim
Conclusion

## Slide 30: Research Directions Enabled by MQSim
MQSim’s accurate models enable many new research studies
  not possible with existing simulators
Fairness and performance effects of inter-flow interference within an SSD
  We study three major sources of contention
    Write cache
    Cached mapping table
    Back end memory resources
  Using I/O flows designed to isolate impact of contention at a single source

## Slide 31: Interference at the Write Cache
Two flows concurrently performing random-access writes
Flow-1 has high cache locality, Flow-2 has poor cache locality
We increase Flow-2 greediness (by adjusting queue depth)
Flow-2
Flow-1
A greedier Flow-2 induces more write cache thrashing, destroying Flow-1’s cache locality

## Slide 32: Interference at the Cached Mapping Table (CMT)
Two flows concurrently reading with different access patterns
Flow-1 sequential; Flow-2 split between sequential, random
We increase randomness of Flow-2, affecting misses to CMT
A more random Flow-2 increases CMT thrashing, significantly lowering the CMT hit rate of Flow-1
Flow-2
Flow-1
Notes: Ask Arash for graphs without hit rate

## Slide 33: Interference at the Back End
Two flows concurrently performing random-access reads
Flow-1 has low intensity, Flow-2 has higher intensity
We increase Flow-2 greediness (by adjusting queue depth)
When Flow-2 is more intense, chip-level queues back up, causing requests from Flow-1 to wait much longer
Flow-2
Flow-1

## Slide 34: Research Directions Enabled by MQSim
MQSim’s accurate models enable many new research studies
  not possible with existing simulators
Fairness and performance effects of inter-flow interference within an SSD
  We study three major sources of contention
    Write cache
    Cached mapping table
    Back-end memory resources
  Using I/O flows designed to isolate impact of contention at a single source
In the paper: application-level studies
  Application-level performance metrics (e.g., IPC, slowdown, fairness)

## Slide 35: Outline
Executive Summary
Looking Inside a Modern SSD
Challenges of Modeling Modern Multi-Queue SSDs
MQSim: A New Simulator for Modern SSDs
Evaluating MQSim Accuracy
Research Directions Enabled by MQSim
Conclusion

## Slide 36: Conclusion
Solid-state drives (SSDs) are evolving to keep pace with performance, storage density demands
  Multi-queue SSDs (MQ-SSDs) use new host protocols (e.g., NVMe)
  New SSDs make use of emerging storage technologies (e.g., PCM, 3D XPoint)
Existing simulators have not kept up with these changes
  They do not support several major features: multi-queue protocols, efficient steady-state SSD models, full end-to-end request latency
  Compared to real MQ-SSDs, best existing simulator has 68–85% error rate
We introduce MQSim, a new open-source simulator
  Models all major features of conventional SSDs and newer MQ-SSDs
  Available with full-system simulator integration: accurate application modeling
  Enables several new research directions
MQSim is highly accurate
  Validated against four real MQ-SSDs
  Error rate for real workloads: 8–18%
http://github.com/CMU-SAFARI/ MQSim

## Slide 37: MQSim: A Framework for Enabling Realistic Studies of Modern Multi-Queue SSD Devices
Arash Tavakkol, Juan Gómez-Luna, Mohammad Sadrosadati, Saugata Ghose, Onur Mutlu
Download the Simulator:
http://github.com/CMU-SAFARI/MQSim

## Slide 38: Computer Architecture Lecture 22c: MQSim
Rakesh Nadig
Prof. Onur Mutlu
ETH Zürich
Fall 2023
8 December 2023

## Slide 39: Backup Slides

## Slide 40: Enabling Higher SSD Performance and Capacity
Solid-state drives (SSDs) are widely used in today’s computer systems
  Data centers
  Enterprise servers
  Consumer devices
I/O demand of both enterprise and consumer applications continues to grow
SSDs are rapidly evolving to deliver improved performance
Host
Host Interface
SATA
NAND Flash
3D XPoint
New NVM

## Slide 41: Simulation Challenges for Modern MQ-SSDs
1. Multi-queue support in modern NVMe SSDs
  The OS I/O scheduler is eliminated
  The device itself is responsible for fairly servicing I/O requests from concurrently-running applications and guaranteeing high responsiveness
Process 1
Process 2
Process 3
SSD Device
Application-level
queues are directly
exposed to the device
No existing SSD simulation tool
supports multi-queue I/O execution

## Slide 42: Defining Slowdown and Fairness for I/O Flows
RTfi: response time of Flow fi
Sfi: slowdown of Flow fi
F: fairness of slowdowns across multiple flows
  0 < F < 1
  Higher F means that system is more fair

## Slide 43: Concurrent Flow Execution in Real Devices

## Slide 44: Concurrent Flow Execution in Real Devices

## Slide 45: Simulation Challenges for Modern MQ-SSDs
The research community needs simulation tools that reliably model these features
State-of-the-art SSD simulators fail to model a number of key properties of modern SSDs
  They implement only the single queue approach
  They do not adequately replicate steady-state behavior  the reported performance values may be far from the long-term results
  They capture only the part of the request latency  do not capture the true request performance of SSDs

## Slide 46: Real Trace Execution Results

## Slide 47: Modeling a Modern MQ-SSD with MQSim
MQSim provides a detailed end-to-end latency model
    A model for all of the request processing steps in modern SSDs
    All of the SSD components are modeled and contributed to the end-to-end latency

## Slide 48: Comparison with Existing Simulators

## Slide 49: Fairness Study Methodology

## Slide 50: Questions
Do you have any plan to support near data processing?
  Yes, we have plans to boost MQSim with support for near data processing
  In six months
Major companies are interested in the performance-cost ratio; How can MQSim help them?
  MQSim can be augmented with a cost model
  Based on the input workload characteristics, MQSim can determine those designs with best performance cost ratio

## Slide 51: Measuring Impact of Interference on Applications
Execute two-application workload bundles
  Applications: file-server (fs), mail-server (ms), web-server (ws), IOzone large file access (io)
  Vary queue fetch size (16 vs. 1024) to model fairness control vs. no control
  Full methodology in the paper
Compare application slowdown, fairness across entire system
Application-level studies with MQSim capture inter-application interference across the entire stack

## Slide 52: Conclusion & Future Work
MQSim: A new simulator that accurately captures the behavior of both modern multi-queue and conventional SATA-based SSDs
MQSim faithfully models a number of critical features absent in existing SSD simulators
MQSim enables a wide range of studies
Future work
  Explore the design space of fairness and QoS techniques in MQ-SSDs
  Design new management mechanism for modern SSDs based on emerging memory technologies

## Slide 53: Mechanism
MQSim is a discrete-event based simulator
Each operation performed by MQSim is an event (Command/Address transfer, Read data out etc.)
A red-black (RB) tree maintains the events in the order of their completion times
Each node of the RB tree has a key which indicates the timestamp to finish and, the value is the callback function
For example, at time 5, a data transfer event starts, and the event will execute for another 5 time-units. The simulator will insert a node <5 + 5, callback> into the tree
At each simulation cycle, the simulator will find the node with the smallest time (value), set the timer to that timestamp, execute the callback function
MQSim supports Real disk traces (e.g., MSR Cambridge Block I/O Traces, YCSB etc.) and Synthetic workloads (generated by the simulation engine)

## Slide 54: Initialization
MQSim components (FTL, SSD Device, TSU etc.) are represented as objects and maintained in a map
The objects in the map are iterated through and corresponding functions are executed
Each object maintains their own version of setup_triggers, start_simulation etc.

## Slide 55: Simulation Engine
Engine.cpp/start_simulation
The callback function is Execute_simulator_event

## Slide 56: Mechanism of MQSim
A simulator event is registered using the Register_sim_event function
Example: An event is registered for sending the Read command and address

## Slide 57: Code Structure
ssdconfig.xml – configuration file that contains the preferred SSD configuration
workload.xml – workload definition file
traces – folder in which the trace files have to be placed
src/sim – contains the files related to the simulation engine
src/nvm_chip – code related to NVM chip. Contains files for die, plane, block and page
src/ssd – contains files related to Flash Translation Layer and Transaction Scheduling Unit
src/host – files related to trace and synthetic workloads, PCIe etc.

## Slide 58: Code Structure
Code flow
  Host -> Data Cache -> Address Translation Unit -> TSU -> Flash Controller -> NVM_Chip
Some important functions:
  Data Cache Manager: process_new_user_requests()
  Address Mapping Unit: translate_lpa_to_ppa_and_dispatch()
  Transaction Scheduling Unit: Schedule()
  Flash Controller: send_command_to_chip()

## Slide 59: SSD Configuration File (ssdconfig.xml)
Host parameters
  PCIe_Lane_Bandwidth: the PCIe bandwidth per lane in GB/s
  PCIe_Lane_Count: the number of PCIe lanes
Device Parameters
  HostInterface_Type: the type of host interface. Range = {NVME, SATA}
  IO_Queue_Depth: the length of the host-side I/O queue.
  Data_Cache_Capacity: the size of the DRAM data cache in bytes
  Ideal_Mapping_Table: if mapping is ideal, all the mapping entries are found in the DRAM and there is no need to read mapping entries from flash
  Transaction_Scheduling_Policy: the transaction scheduling policy that is used in the SSD back end. Range = {OUT_OF_ORDER as defined in the Sprinkler (Jung et.al., HPCA 2014), PRIORITY_OUT_OF_ORDER which implements OUT_OF_ORDER and NVMe priorities}

## Slide 60: SSD Configuration File (ssdconfig.xml)
Device Parameters
  Flash_Channel_Count: the number of flash channels in the SSD back end
  Flash_Channel_Width: the width of each flash channel in bytes
  Chip_No_Per_Channel: the number of flash chips attached to each channel in the SSD back end
NAND Parameters
  Flash_Technology: Range = {SLC, MLC, TLC}.
  Page read latency for LSB, CSB and MSB pages (in nanoseconds)
  Page program latency (in nanoseconds)
  Block_Erase_Latency: erase latency in nanoseconds
  Block_PE_Cycles_Limit: the PE limit of each flash block

## Slide 61: SSD Configuration File (ssdconfig.xml)
NAND Parameters
  Die_No_Per_Chip: the number of dies in each flash chip
  Plane_No_Per_Die: the number of planes in each die
  Block_No_Per_Plane: the number of flash blocks in each plane
  Page_No_Per_Block: the number of physical pages in each flash block
  Page_Capacity: the size of each physical flash page in bytes
  Page_Metadata_Capacity: the size of the metadata area of each physical flash page in bytes

## Slide 62: Trace-based workload configuration

## Slide 63: Synthetic workload configuration

## Slide 64: MQSim Output File

## Slide 65: MQSim usage
Linux
  $ make
  $ ./MQSim -i <SSD Configuration File> -w <Workload Definition File>
Windows
  Open the MQSim.sln solution file in MS Visual Studio 2017 or later.
  Set the Solution Configuration to Release (it is set to Debug by default).
  Compile the solution.
  Run the generated executable file (e.g., MQSim.exe) either in command line mode or by clicking the MS Visual Studio run button. Please specify the paths to the files containing the 1) SSD configurations, and 2) workload definitions.
  $ MQSim.exe -i <SSD Configuration File> -w <Workload Definition File>